## Slide 1: ESD Presentation
JEEVARAM K
RISHI S PHAYE
M.E EMBEDDED SYSTEM

## Slide 2
AUTO DRONE

## Slide 3
Contents
ABSTRACT
ARCHITECTURE
PARTIAL SYSTEMS
SUBSYSTEMS

## Slide 4
The project is aimed at designing a common architecture in terms of hardware and software for an automated drone.
The system is divided into two parts, a communication layer and the subsystem layer.
For every feature (or) operation, a separate subsystem is designed and attached with the main controller.
The main controller receives all the inputs from various subsystems and makes driving decision based on those inputs. The output of main controller is just four PWM signal each of which operates Elevator, Aileron, Rudder and Throttle.
In this project, the following subsystems are planned, automated driving subsystem, user communication subsystem, Localization subsystem and Obstacle avoidance subsystem.
All the above said subsystems are attached to the main controller through a communication bus based on I2C.
Abstract

## Slide 5
Architecture
Main/Master Controller
Obstacle Avoidance Subsystem
Automated Driving Subsystem
Communication Subsystem
LIDAR/Ultrasonic Sensor System
GPS and IMU Units
Wi-Fi
I2C Bus
Elevator
Rudder
Aileron
Throttle
(Mimics the input of RC
Controller)

## Slide 6
Partial System
The communication layer
The subsystem layer

## Slide 7
I2C Bus
GPS Subsystem
GPS Receiver
IMU Subsystem
IMU Sensor (BNO055)
Main/Master Controller

## Slide 8
SUBSYSTEMS
1.Subsystem Address Ranges Definition
Start Address | End Address | Type of Subsystem
0x10 | 0x19 | Relative Position Subsystem
0x20 | 0x25 | GPS Subsystem
0x26 | 0x29 | External RF Communication Subsystem
0x30 | 0x39 | Obstacle Avoidance Subsystem
0x40 | 0x49 | Health Monitoring Subsystem
0x50 | 0x59 | Communication Subsystem

## Slide 9
2.GPS Subsystem Register Structure
Register Address | Data Type and Length | Description
0x01 | 1 – U Int | No of Satellites Connected
0x02 | 4 – Float | Latitude
0x03 | 4 – Float | Longitude
0x04 | 4 – Float | Altitude
0x05 | 4 – Float | Horizontal Accuracy
0x06 | 4 – Float | Vertical Accuracy
0x07 | 4 - Float | Refresh Rate (in ms)

## Slide 10
3.Relative Position Subsystem Register Structure
Register Address | Data Type and Length | Description
0x01 | 1 – U Int | Type of Subsystem
0x02 | 4 – Float | X-Value
0x03 | 4 – Float | Y-Value
0x04 | 4 – Float | Z-Value
0x05 | 4 – Float | Refresh Rate (in ms)

## Slide 11
4.Obstacle Avoidance Subsystem Register Structure
Register Address | Data Type and Length | Description
0x01 | 1 – U Int | Reserved (Type of Subsystem)
0x02 | 4 – Float | Direction of Obstacle (Degrees)
0x03 | 4 – Float | Distance to Impact (Metres)
0x04 | 4 – Float | Refresh Rate (in ms)

## Slide 12
5.Communication Subsystem Register Structure
Register Address | Data Type and Length | Description
0x01 | 1 – U Int | Type of Communication
0x02 | 4 – Float | Latitude
0x03 | 4 – Float | Longitude
0x04 | 4 – Float | Altitude
0x05 | 1 – U Int | Back to Origin

## Slide 13
6.External RF Communication Register Structure
Register Address | Data Type and Length | Description
0x01 | 1 – U Int | Type of RF
0x02 | 2 – U Int | Channel 1
0x03 | 2 – U Int | Channel 2
0x04 | 2 – U Int | Channel 3
0x05 | 2 – U Int | Channel 4
0x06 | 2 – U Int | Channel 5
0x07 | 2 – U Int | Channel 6

## Slide 14
FUTURE SCOPE
In this architecture, additional features can also be added since the communication bus is I2C and the master controller can be configured after adding the additional subsystems to the bus and integrated with the system easily.
At the end, the Master controller combines all the inputs from multiple subsystems and takes decision based on its configuration input.