## Slide 1: ESD Presentation
Jeevaraam K
Rishi S Phaye
M.E. EMBEDDED SYSTEM

## Slide 2
AUTO DRONE

## Slide 3
Abstract
Aim and Objectives
Proposed Methodology
Block Diagram
Architecture Overview
List of Subsystems
Individual Subsystems
Currently Implemented Subsystems
Results and Output
Conclusion
Contents

## Slide 4
Aimed at designing a common architecture in terms of hardware and software for an automated drone.
Divided into two parts, a Main Controller and the subsystem layer.
For every feature (or) operation, a separate subsystem is designed and attached with the main controller.
Main controller receives all the inputs from various subsystems and makes driving decision based on those inputs.
All the above said subsystems are attached to the main controller through a communication bus based on I2C.
Abstract

## Slide 5
Aim
To design a drone that can travel on its own from one place to another, Hence Auto-Drone.
Objectives
To design a common architecture for autonomous drone
To implement a Communication Sub-system corresponding to the above architecture
To implement a Autonomous driving sub-system corresponding to above architecture
To implement Main Controller program corresponding to above architecture
To make the subsystems work with the main frame.
To identify the shortest path between the destination and source.
To tackle the obstacles using AI.
Aim and Objectives

## Slide 6
Proposed Methodology

## Slide 7
Main/Master Controller
Obstacle Avoidance Subsystem
Automated Driving Subsystem
Communication Subsystem
LIDAR/Ultrasonic Sensor System
GPS and IMU Units
Wi-Fi
I2C Bus
Elevator
Rudder
Aileron
Throttle
(Mimics the input of RC
Controller)
Block Diagram

## Slide 8
The project aims to design an architecture where a master controller receives data from all the attached sub-systems
In the initial stages, three subsystems are planned.
An autonomous driving sub-system,
A communication sub-system
An obstacle avoidance sub-system.
Architecture Overview

## Slide 9
The communication sub-system is aimed at providing communication between the drone and the user
The autonomous driving subsystem contains two input sensors, a GPS receiver and an IMU unit.
The obstacle avoidance sub-sytems constantly looks for any obstacles it gets in its way and alerts the Main controller if any obstacle is there and the Main controller takes actions based on the direction and closeness of the obstacle.

## Slide 10
Individual Subsystems

## Slide 11
Subsystem Address Ranges Definition
Start Address | End Address | Type of Subsystem
0x10 | 0x19 | Relative Position Subsystem
0x20 | 0x25 | GPS Subsystem
0x26 | 0x29 | External RF Communication Subsystem
0x30 | 0x39 | Obstacle Avoidance Subsystem
0x40 | 0x49 | Health Monitoring Subsystem
0x50 | 0x59 | Communication Subsystem

## Slide 12
GPS Subsystem Register Structure
Register Address | Data Type and Length | Description
0x01 | 1 – U Int | No of Satellites Connected
0x02 | 4 – Float | Latitude
0x03 | 4 – Float | Longitude
0x04 | 4 – Float | Altitude
0x05 | 4 – Float | Horizontal Accuracy
0x06 | 4 – Float | Vertical Accuracy
0x07 | 4 - Float | Refresh Rate (in ms)

## Slide 13
Relative Position Subsystem Register Structure
Register Address | Data Type and Length | Description
0x01 | 1 – U Int | Type of Subsystem
0x02 | 4 – Float | X-Value
0x03 | 4 – Float | Y-Value
0x04 | 4 – Float | Z-Value
0x05 | 4 – Float | Refresh Rate (in ms)

## Slide 14
Obstacle Avoidance Subsystem Register Structure
Register Address | Data Type and Length | Description
0x01 | 1 – U Int | Reserved (Type of Subsystem)
0x02 | 4 – Float | Direction of Obstacle (Degrees)
0x03 | 4 – Float | Distance to Impact (Metres)
0x04 | 4 – Float | Refresh Rate (in ms)

## Slide 15
Communication Subsystem Register Structure
Register Address | Data Type and Length | Description
0x01 | 1 – U Int | Type of Communication
0x02 | 4 – Float | Latitude
0x03 | 4 – Float | Longitude
0x04 | 4 – Float | Altitude
0x05 | 1 – U Int | Back to Origin

## Slide 16
External RF Communication Register Structure
Register Address | Data Type and Length | Description
0x01 | 1 – U Int | Type of RF
0x02 | 2 – U Int | Channel 1
0x03 | 2 – U Int | Channel 2
0x04 | 2 – U Int | Channel 3
0x05 | 2 – U Int | Channel 4
0x06 | 2 – U Int | Channel 5
0x07 | 2 – U Int | Channel 6

## Slide 17
Currently Implemented Subsystem
I2C Bus
GPS Subsystem
GPS Receiver
IMU Subsystem
IMU Sensor (BNO055)
Main/Master Controller

## Slide 18
Current Status of development. (Output and status can be changed if we get any output and obtain result before our presentation)
Results and Output

## Slide 19
Points complementing the data given in Aim and Objectives slide
Conclusion

## Slide 20
In this architecture, additional features can also be added since the communication bus is I2C and the master controller can be configured after adding the additional subsystems to the bus and integrated with the system easily.
At the end, the Master controller combines all the inputs from multiple subsystems and takes decision based on its configuration input.
Future Scope

## Slide 21
THANK YOU